## Slide 1
TCP/IP Protocol Suite
1
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Transmission
Control
Protocol (TCP)

## Slide 2: OBJECTIVES:
TCP/IP Protocol Suite
2
To introduce TCP as a protocol that provides reliable stream delivery service.
To define TCP features and compare them with UDP features.
To define the format of a TCP segment and its fields.
To show how TCP provides a connection-oriented service, and show the segments exchanged during connection establishment and connection termination phases.
To introduce windows in TCP that are used for flow and error control.

## Slide 3: OBJECTIVES (continued):
TCP/IP Protocol Suite
3
To discuss how TCP implements flow control in which the receive window controls the size of the send window.
To discuss error control used by TCP during the data transmission phase.
To discuss how TCP controls the congestion in the network using different strategies.
To list and explain the purpose of each timer in TCP.
To discuss options in TCP and show how TCP can provide selective acknowledgment using the SACK option.

## Slide 4
TCP/IP Protocol Suite
4
Chapter Outline
TCP Services
TCP Features
Segment
A TCP Connection
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 5
TCP/IP Protocol Suite
5
15-1 TCP SERVICES
Figure 15.1 shows the relationship of TCP to the other protocols in the TCP/IP protocol suite. TCP lies between the application layer and the network layer, and serves as the intermediary between the application programs and the network operations.

## Slide 6
TCP/IP Protocol Suite
6
Figure 15.1 TCP/IP protocol suite

## Slide 7
TCP/IP Protocol Suite
7
Topics Discussed in the Section
Process-to-Process Communication
Stream Delivery Service
Full-Duplex Communication
Multiplexing and Demultiplexing
Connection-Oriented Service
Reliable Service

## Slide 8
TCP/IP Protocol Suite
8

## Slide 9
TCP/IP Protocol Suite
9
Figure 15.2 Stream delivery

## Slide 10
TCP/IP Protocol Suite
10
Figure 15.3 Sending and receiving buffers

## Slide 11
TCP/IP Protocol Suite
11
Figure 15.4 TCP segments

## Slide 12
Full duplex communication
Multiplexing and demultiplexing
Connection oriented service
Reliable service: it uses ack mechanism to check the safe and sound arrival of data
TCP/IP Protocol Suite
12

## Slide 13
TCP/IP Protocol Suite
13
15-2 TCP FEATURES
To provide the services mentioned in the previous section, TCP has several features that are briefly summarized in this section and discussed later in detail.

## Slide 14
TCP/IP Protocol Suite
14
Topics Discussed in the Section
Numbering System
Flow Control
Error Control
Congestion Control

## Slide 15
Numbering System
Although the TCP software keeps track of the segments being transmitted or received, there is no field for a segment number value in the segment header. Instead, there are two fields called the sequence number and the acknowledgment number. These two fields refer to a byte number and not a segment number.
TCP/IP Protocol Suite
15

## Slide 16
Byte Number
TCP numbers all data bytes (octets) that are transmitted in a connection.
Numbering is independent in each direction. When TCP receives bytes of data from a process, TCP stores them in the sending buffer and numbers them.
The numbering does not necessarily start from 0. Instead, TCP chooses an arbitrary number between 0 and 2^32− 1 for the number of the first byte.
For example, if the number happens to be 1,057 and the total data to be sent is 6,000 bytes, the bytes are numbered from 1,057 to 7,056.
We will see that byte numbering is used for flow and error control

## Slide 17
TCP/IP Protocol Suite
17
The bytes of data being transferred in each connection are numbered by TCP.
The numbering starts with an arbitrarily generated number.
Note

## Slide 18
TCP/IP Protocol Suite
18
Suppose a TCP connection is transferring a file of 5,000 bytes. The first byte is numbered 10,001. What are the sequence numbers for each segment if data are sent in five segments, each carrying 1,000 bytes?
Solution
The following shows the sequence number for each segment:
Example 15.1

## Slide 19
TCP/IP Protocol Suite
19
The value in the sequence number field of a segment defines the number assigned to the first data byte contained in that segment.
Note
Data byte 1
Data byte 3
Data byte 2
Data byte 4
Data byte 5
segment

## Slide 20
TCP/IP Protocol Suite
20
The value of the acknowledgment field in a segment defines the number of the next byte a party expects to receive.
The acknowledgment number is cumulative.
Note

## Slide 21
TCP/IP Protocol Suite
21
15-3 SEGMENT
Before discussing TCP in more detail, let us discuss the TCP packets themselves. A packet in TCP is called a segment.

## Slide 22
TCP/IP Protocol Suite
22
Topics Discussed in the Section
Format
Encapsulation

## Slide 23
TCP/IP Protocol Suite
23
Figure 15.5 TCP segment format

## Slide 24
TCP/IP Protocol Suite
24
Figure 15.6 Control field

## Slide 25
TCP/IP Protocol Suite
25
Figure 15.7 Pseudoheader added to the TCP segment

## Slide 26
TCP/IP Protocol Suite
26
The use of the checksum in TCP is mandatory.
Note

## Slide 27
TCP/IP Protocol Suite
27
Figure 15.8 Encapsulation

## Slide 28
TCP/IP Protocol Suite
28
15-4 A TCP CONNECTION
TCP is connection-oriented.
It establishes a virtual path between the source and destination.
All of the segments belonging to a message are then sent over this virtual path.
You may wonder how TCP, which uses the services of IP, a connectionless protocol, can be connection-oriented. The point is that a TCP connection is virtual, not physical. TCP operates at a higher level.
TCP uses the services of IP to deliver individual segments to the receiver, but it controls the connection itself. If a segment is lost or corrupted, it is retransmitted.

## Slide 29
TCP/IP Protocol Suite
29
Topics Discussed in the Section
Connection Establishment
Data Transfer
Connection Termination
Connection Reset: RST FLAG

## Slide 30: three-way handshake
A three-way handshake is a method used in a TCP/IP network to create a connection between a local host/client and server. It is a three-step method that requires both the client and server to exchange SYN and ACK (acknowledgment) packets before actual data communication begins.
A three-way handshake is also known as a TCP handshake.
30

## Slide 31
TCP/IP Protocol Suite
31
Figure 15.9 Connection establishment using three-way handshake

## Slide 32
TCP/IP Protocol Suite
32

## Slide 33
A client node sends a SYN data packet over an IP network to a server on the same or an external network. The objective of this packet is to ask/infer if the server is open for new connections.
The target server must have open ports that can accept and initiate new connections. When the server receives the SYN packet from the client node, it responds and returns a confirmation receipt – the ACK packet or SYN/ACK packet.
The client node receives the SYN/ACK from the server and responds with an ACK packet.
Upon completion of this process, the connection is created and the host and server can communicate.
TCP/IP Protocol Suite
33

## Slide 34
TCP/IP Protocol Suite
34
A SYN segment cannot carry data, but it consumes one sequence number.
Note

## Slide 35
TCP/IP Protocol Suite
35
A SYN + ACK segment cannot carry data, but does consume one sequence number.
Note

## Slide 36
TCP/IP Protocol Suite
36
An ACK segment, if carrying no data, consumes no sequence number.
Note

## Slide 38
client 1
server
client 2
client 3
client n
syn
syn
syn
syn
syn+ ack
syn+ ack
syn+ ack
syn+ ack

## Slide 39
TCP/IP Protocol Suite
39

## Slide 40
TCP/IP Protocol Suite
40
Figure 15.10 Data Transfer
Connection establishment
Connection termination

## Slide 41
TCP/IP Protocol Suite
41
Figure 15.11 Connection termination using three-way handshake
2 options for termination:
3 way handshaking
Four way handshaking with a half close option

## Slide 42
TCP/IP Protocol Suite
42

## Slide 43
TCP/IP Protocol Suite
43

## Slide 44
TCP/IP Protocol Suite
44

## Slide 45
TCP/IP Protocol Suite
45
The FIN segment consumes one sequence number if it does not carry data.
Note

## Slide 46
TCP/IP Protocol Suite
46
The FIN + ACK segment consumes one sequence number if it does not carry data.
Note

## Slide 47
TCP/IP Protocol Suite
47
Figure 15.12 Half-Close

## Slide 48
TCP/IP Protocol Suite
48

## Slide 49: Connection reset
Denying a connection
Aborting a connection
Termination an idle connection
TCP/IP Protocol Suite
49

## Slide 50
TCP/IP Protocol Suite
50
15-6 WINDOWS IN TCP
Before discussing data transfer in TCP and the issues such as flow, error, and congestion control, we describe the windows used in TCP. TCP uses two windows (send window and receive window) for each direction of data transfer, which means four windows for a bidirectional communication. To make the discussion simple, we make an assumption that communication is only unidirectional; the bidirectional communication can be inferred using two unidirectional communications with piggybacking.

## Slide 51
TCP/IP Protocol Suite
51
Topics Discussed in the Section
Send Window
Receive Window

## Slide 52
TCP/IP Protocol Suite
52
Figure 15.22 Send window in TCP

## Slide 53
TCP/IP Protocol Suite
53
Figure 15.23 Receive window in TCP

## Slide 54
TCP/IP Protocol Suite
54
15-7 FLOW CONTROL
As discussed in Chapter 13, flow control balances the rate a producer creates data with the rate a consumer can use the data. TCP separates flow control from error control. In this section we discuss flow control, ignoring error control. We temporarily assume that the logical channel between the sending and receiving TCP is error-free. Figure 15.24 shows unidirectional data transfer between a sender and a receiver; bidirectional data transfer can be deduced from unidirectional one as discussed in Chapter 13.

## Slide 55
TCP/IP Protocol Suite
55
Figure 15.24 TCP/IP protocol suite

## Slide 56
TCP/IP Protocol Suite
56
Figure 15.25 An example of flow control

## Slide 57
TCP/IP Protocol Suite
57
15-8 ERROR CONTROL
TCP is a reliable transport layer protocol. This means that an application program that delivers a stream of data to TCP relies on TCP to deliver the entire stream to the application program on the other end in order, without error, and without any part lost or duplicated.
Error control in TCP is achieved through the use of three tools: checksum, acknowledgment, and time-out.

## Slide 58
TCP/IP Protocol Suite
58
Topics Discussed in the Section
Checksum
Acknowledgment: cumulative, SACK.
Retransmission: RTO, 3 DUPLICATE ACKS.
Out-of-Order Segments:
NORMAL OPERATIONS
LOST SEGMENT
FAST RETRANMISSION
AUTOMATICALLY CORRECTED LOST ACK
LOST ACK CORRECTED BY RESENDING A SEGMENT

## Slide 59
Round Trip Time (RTT) is defined as time between packet send and it's Ack is received . ... Retransmission Time Out (RTO) is the time set for ACK of particular packet to be received , after this time packet is declared as lost and is retransmitted.

## Slide 60
TCP/IP Protocol Suite
60
Figure 15.29 Normal operation

## Slide 61
TCP/IP Protocol Suite
61
Figure 15.30 Lost segment

## Slide 62
TCP/IP Protocol Suite
62
The receiver TCP delivers only ordered data to the process.
Note

## Slide 63
TCP/IP Protocol Suite
63
Figure 15.31 Fast retransmission

## Slide 64
TCP/IP Protocol Suite
64
Figure 15.32 Lost acknowledgment

## Slide 65
TCP/IP Protocol Suite
65
Figure 15.33 Lost acknowledgment corrected by resending a segment

## Slide 66
TCP/IP Protocol Suite
66
15-9 CONGESTION CONTROL
Congestion control in TCP uses a congestion window and a congestion policy that avoid congestion and detect and alleviate congestion after it has occurred.

## Slide 67
TCP/IP Protocol Suite
67
Topics Discussed in the Section
Congestion Window
Congestion Policy
Congestion Window (cwnd) is a TCP state variable that limits the amount of data the TCP can send into the network before receiving an ACK.
The Receiver Window (rwnd) is a variable that advertises the amount of data that the destination side can receive.
Together, the two variables are used to regulate data flow in TCP connections, minimize congestion, and improve network performance.

## Slide 68
TCP/IP Protocol Suite
68

## Slide 69
TCP/IP Protocol Suite
69

## Slide 70
TCP/IP Protocol Suite
70
Figure 15.34 Slow start, exponential increase

## Slide 71
TCP/IP Protocol Suite
71

## Slide 72
TCP/IP Protocol Suite
72
In the slow start algorithm, the size of the congestion window increases exponentially until it reaches a threshold.
Note

## Slide 73
TCP/IP Protocol Suite
73
Figure 15.35 Congestion avoidance, additive increase

## Slide 74
TCP/IP Protocol Suite
74

## Slide 75
TCP/IP Protocol Suite
75
In the congestion avoidance algorithm the size of the congestion window
increases additively until
congestion is detected.
Note

## Slide 77
TCP/IP Protocol Suite
77
15-10 TCP TIMERS
To perform its operation smoothly, most TCP implementations use at least four timers .
Timers used by TCP to avoid excessive delays during communication are called as TCP Timers.

## Slide 78
TCP/IP Protocol Suite
78
Topics Discussed in the Section
Retransmission Timer
Persistence Timer
Keepalive Timer
TIME-WAIT Timer

## Slide 79
TCP/IP Protocol Suite
79
Figure 15.38 TCP timers

## Slide 80
Retransmission Timer
To retransmit lost segments, TCP employs one retransmission timer (for the whole connection period) that handles the retransmission time-out (RTO), the waiting time for an acknowledgment of a segment. We can define the following rules for the retransmission timer:
1. When TCP sends the segment in front of the sending queue, it starts the timer.
2. When the timer expires, TCP resends the first segment in front of the queue, and restarts the timer.
3. When a segment (or segments) are cumulatively acknowledged, the segment (or segments) are purged from the queue.
4. If the queue is empty, TCP stops the timer; otherwise, TCP restarts the timer.
TCP/IP Protocol Suite
80

## Slide 81
Sender starts a time out timer after transmitting a TCP segment to the receiver.
If sender receives an acknowledgement before the timer goes off, it stops the timer.
If sender does not receives any acknowledgement and the timer goes off, then TCP Retransmission occurs.
Sender retransmits the same segment and resets the timer.
The value of time out timer is dynamic and changes with the amount of traffic in the network.
Time out timer is also called as Retransmission Timer.

## Slide 82
Measured RTT
Smoothed RTT
TCP/IP Protocol Suite
82

## Slide 83
Measured RTT(RTTm) – The measured round-trip time for a segment is the time required for the segment to reach the destination and be acknowledged, although the acknowledgment may include other segments.
Smoothed RTT(RTTs) – It is the weighted average of RTTm. RTTm is likely to change and its fluctuation is so high that a single measurement cannot be used to calculate RTO.

## Slide 84
TCP/IP Protocol Suite
84

## Slide 85
TCP/IP Protocol Suite
85

## Slide 86
TCP/IP Protocol Suite
86
D

## Slide 87
TCP/IP Protocol Suite
87
In TCP, there can be only one RTT measurement in progress at any time.
Note

## Slide 88
TCP/IP Protocol Suite
88
Let us give a hypothetical example. Figure 15.39 shows part of a connection. The figure shows the connection establishment and part of the data transfer phases.
1. When the SYN segment is sent, there is no value for RTTM, RTTS, or RTTD. The value of RTO is set to 6.00 seconds. The following shows the value of these variable at this moment:
Example 15.3
2. When the SYN+ACK segment arrives, RTTM is measured and is equal to 1.5 seconds.

## Slide 89
TCP/IP Protocol Suite
89
Figure 15.39 Example 15.3

## Slide 90
TCP/IP Protocol Suite
90
3. When the first data segment is sent, a new RTT measurement starts. No RTT measurement starts for the second data segment because a measurement is already in progress. The arrival of the last ACK segment is used to calculate the next value of RTTM. Although the last ACK segment acknowledges both data segments (cumulative), its arrival finalizes the value of RTTM for the first segment. The values of these variables are now as shown below.
Example 15.3 Continued
0.75

## Slide 91
TCP/IP Protocol Suite
91
Figure 15.39 Example 15.3

## Slide 92
TCP/IP Protocol Suite
92

## Slide 93
TCP/IP Protocol Suite
93
Figure 15.40 is a continuation of the previous example. There is retransmission and Karn’s algorithm is applied.
The first segment in the figure is sent, but lost. The RTO timer expires after 4.74 seconds. The segment is retransmitted and the timer is set to 9.48, twice the previous value of RTO. This time an ACK is received before the time-out. We wait until we send a new segment and receive the ACK for it before recalculating the RTO (Karn’s algorithm).
Example 15.4

## Slide 94
TCP/IP Protocol Suite
94
Figure 15.40 Example 15.4

## Slide 95
TCP/IP Protocol Suite
95

## Slide 96
TCP/IP Protocol Suite
96

## Slide 97
sender
recvr
Win size=0
Ack=winsize=40
deadlock

## Slide 98
sender
recvr
Win size=0
Ack=winsize=40
deadlock
Persistence timer

## Slide 99
sender
recvr
Win size=0
Persistence timer starts
Persistence timer stops
probe
Ack for probe
probe
If ack does not come,,,, one more probe will be send and Persistence timer is doubled

## Slide 100
TCP/IP Protocol Suite
100

## Slide 101
client
server
keepalive timer

## Slide 102
https://www.gatevidyalay.com/silly-window-syndrome-nagles-algorithm/

## Slide 103
TCP/IP Protocol Suite
103
15-11 OPTIONS
The TCP header can have up to 40 bytes of optional information. Options convey additional information to the destination or align other options. We can define two categories of options: 1-byte options and multiple-byte options. The first category contains two types of options: end of option list and no operation. The second category, in most implementations, contains five types of options: maximum segment size, window scale factor, timestamp, SACK-permitted, and SACK (see Figure 15.41).

## Slide 104
TCP/IP Protocol Suite
104
Figure 15.41 Options

## Slide 105
TCP/IP Protocol Suite
105

## Slide 106
TCP/IP Protocol Suite
106
Figure 15.42 End-of-option option

## Slide 107
TCP/IP Protocol Suite
107
EOP can be used only once.
Note

## Slide 108
TCP/IP Protocol Suite
108
Figure 15.43 No-operation option

## Slide 109
TCP/IP Protocol Suite
109
NOP can be used more than once.
Note

## Slide 110
TCP/IP Protocol Suite
110
Figure 15.44 Minimum-segment-size option

## Slide 111
TCP/IP Protocol Suite
111
Figure 15.45 Window-scale-factor option

## Slide 112
TCP/IP Protocol Suite
112

## Slide 113
TCP/IP Protocol Suite
113
The value of the window scale factor can be determined only during connection
establishment; it does not change during the connection.
Note

## Slide 114
TCP/IP Protocol Suite
114
Figure 15.46 Timestamp option

## Slide 115
TCP/IP Protocol Suite
115
One application of the timestamp option is the calculation of round-trip time (RTT).
Note

## Slide 116
TCP/IP Protocol Suite
116

## Slide 117
TCP/IP Protocol Suite
117
Figure 15.48 SACK

## Slide 118
TCP/IP Protocol Suite
118

## Slide 119
TCP/IP Protocol Suite
119
Let us see how the SACK option is used to list out-of-order blocks. In Figure 15.49 an end has received five segments of data.
Example 15.6

## Slide 120
TCP/IP Protocol Suite
120
Figure 15.49 Example 15.6

## Slide 121
TCP/IP Protocol Suite
121
Figure 15.50 shows how a duplicate segment can be detected with a combination of ACK and SACK. In this case, we have some out-of-order segments (in one block) and one duplicate segment. To show both out-of-order and duplicate data, SACK uses the first block, in this case, to show the duplicate data and other blocks to show out-of-order data. Note that only the first block can be used for duplicate data. The natural question is how the sender, when it receives these ACK and SACK values, knows that the first block is for duplicate data (compare this example with the previous example). The answer is that the bytes in the first block are already acknowledged in the ACK field; therefore, this block must be a duplicate.
Example 15.7

## Slide 122
TCP/IP Protocol Suite
122
Figure 15.50 Example 15.7

## Slide 123
TCP/IP Protocol Suite
123
Figure 15.51 shows what happens if one of the segments in the out-of-order section is also duplicated. In this example, one of the segments (4001:5000) is duplicated.
The SACK option announces this duplicate data first and then the out-of-order block. This time, however, the duplicated block is not yet acknowledged by ACK, but because it is part of the out-of-order block (4001:5000 is part of 4001:6000), it is understood by the sender that it defines the duplicate data.
Example 15.8

## Slide 124
TCP/IP Protocol Suite
124
Figure 15.51 Example 15.8

## Slide 125: TCP PACKAGE
TCP/IP Protocol Suite
125

## Slide 126
TCP/IP Protocol Suite
126
Topics Discussed in the Section
Transmission Control Block TCBs
Timers
Main Module
Input Processing Module
Output Processing Module

## Slide 127
TCP/IP Protocol Suite
127
Figure 15.52 TCP PACKAGE

## Slide 128
TCP/IP Protocol Suite
128

## Slide 129
TCP/IP Protocol Suite
129

## Slide 130
TCP/IP Protocol Suite
130
established

## Slide 131
TCP/IP Protocol Suite
131

## Slide 132
TCP/IP Protocol Suite
132

## Slide 133
TCP/IP Protocol Suite
133

## Slide 134
TCP/IP Protocol Suite
134

## Slide 135
TCP/IP Protocol Suite
135

## Slide 136
TCP/IP Protocol Suite
136

## Slide 137
TCP/IP Protocol Suite
137

## Slide 138
TCP/IP Protocol Suite
138

## Slide 139
TCP/IP Protocol Suite
139

## Slide 140
TCP/IP Protocol Suite
140